## Slide 1
TASK 2 • GEOLAND AI
FarmAI – GeoLand Intelligence
Autonomous Multimodal GeoAI & Land Document Due Diligence Platform
Instant bilingual OCR, FMB ladder vectorization, cadastral GIS cross-reconciliation, statutory buffer auditing, and tamper-evident Title Integrity Risk Scoring (0–100).
Bilingual OCR (Tamil/Eng)
FMB Ladder Vectorizer
3-Way Spatial Reconciliation
30m Waterbody Buffer Check
AWS Cloud Integrated
Presented by: Team 63 (FAI-TCE-Team-63) | FarmAI Research & Engineering Team Core Stack: FastAPI, Shapely, Leaflet, React 18, Vite, Amazon Textract, S3, DynamoDB Repository: https://github.com/krishnakanthm2805/farmai_project.git

## Slide 2
EXECUTIVE CHALLENGE
The Problem: Manual Land Due Diligence is Broken
FarmAI Platform • Autonomous Due Diligence & Cadastral Reconciliation
CONFIDENTIAL • TEAM 63
1. Heterogeneous Data Silos
Title documents are manual, hand-scanned e-Pattas (Form 10), Chitta, and Sale Deeds in Tamil and English.
They exist completely isolated from government GIS Cadastral shapefiles and legacy surveyor sketches.
2. Complex FMB Survey Ladders
Field Measurement Books (FMB) use century-old hand-drawn G-lines and offset ladder tables.
Extracting polygon vertices and cross-checking area against registered claims takes days per parcel.
3. Hidden Encroachments & Risk
Severe statutory liabilities often go undetected:
• Illegal intrusions into 30m waterbody buffers (Kanmois/Lakes).
• Road Right-of-Way (RoW) violations.
• Unchecked monsoon flood inundation zones.
The Result: Financial institutions, solar farm developers, and infrastructure agencies face weeks of delay, high legal costs, and multi-crore non-performing loans (NPLs) from contested land titles.

## Slide 3
CORE VALUE PROPOSITION
The FarmAI Solution: Autonomous GeoAI Due Diligence
FarmAI Platform • Autonomous Due Diligence & Cadastral Reconciliation
CONFIDENTIAL • TEAM 63
[1] Sub-Second Ingestion & OCR
Extracts survey numbers, sub-divisions, pattadar names, extent (Hectares-Ares/Cents to Acres/m2), and statutory boundaries across Tamil & English formats.
[2] FMB Ladder Vectorization
Converts raw surveyor ladder tables (G-line base, left/right perpendicular offsets) into precise EPSG-compliant metric vector polygons using the Shoelace formula.
[3] 3-Way Spatial Reconciliation
Cross-checks Document Claimed Extent vs. Cadastral GIS Polygon vs. FMB Surveyed Polygon. Automatically flags any variance exceeding permissible 2.0% threshold.
[4] Statutory Buffer Auditing
Shapely computational geometric intersection algorithms instantly check for 30m waterbody buffers and 15m road setbacks.
[5] Objective Title Risk Score (0-100)
Generates an objective, weighted risk penalty index categorizing titles into Tier 1 (Clean), Tier 2 (Caution), or Tier 3 (Critical Risk/Rejected).
[6] Automated Audit Certificate
Produces tamper-evident digital due diligence audit reports with parcel geometry snapshots and audit hashes ready for legal sign-off.

## Slide 4
SYSTEM ARCHITECTURE
End-to-End Multi-Tier System Architecture
FarmAI Platform • Autonomous Due Diligence & Cadastral Reconciliation
CONFIDENTIAL • TEAM 63
1. PRESENTATION LAYER
React 18 + Vite + Tailwind CSS v4 + Leaflet GIS
• Interactive Satellite & Hybrid GIS Explorer (Esri World Imagery)
• 396 Parcel Cadastral Map Overlays with Real-Time Centroid Fly-To
• Multimodal Document OCR & Discrepancy Matrix Visualizer
• Automated Due Diligence Audit Certificate Modal (PDF/Print Ready)
2. API & GATEWAY LAYER
FastAPI (Asynchronous Python 3.11/3.13) + Uvicorn
• High-performance non-blocking async REST endpoints (/api/analyze)
• 8MB Chunked Disk-Streaming Ingestion Worker for 500MB+ datasets
• CORS middleware, input sanitization, and structured JSON schemas
• Health check and module status diagnostics (/api/health)
3. CORE GEOAI ENGINES
Shapely Geometry, NumPy, PyPDF, Pytesseract, SRTM DEM
• Engine 1: Multimodal OCR & Bilingual Tamil/English NLP Parser
• Engine 2: FMB G-Line Coordinate Vectorizer (Shoelace Formula)
• Engine 3: Spatial Cadastral Reconciler & 3-Way Cross Checker
• Engine 4: Raster DEM & Hydrological Flood Inundation Engine
• Engine 5: Title Integrity Risk Scorer (0-100 Penalty Matrix)
4. CLOUD & DATA LAYER
Amazon Web Services (AWS ap-south-1 Mumbai) + GeoJSON
• Amazon Textract: High-accuracy OCR & document intelligence
• Amazon S3: Land document buffer and multi-page PDF processing
• Amazon DynamoDB: Tamper-evident title audit records and trail
• 12 Geospatial Layers: Cadastral parcels, roads, waterbodies, parks

## Slide 5
DEEP-DIVE ENGINES 1-3
Core Engines: Document OCR, FMB & Spatial Geometry
FarmAI Platform • Autonomous Due Diligence & Cadastral Reconciliation
CONFIDENTIAL • TEAM 63
ENGINE 1
Multimodal OCR & Bilingual Parser
File: backend/ocr_engine.py
• Bilingual Tokenizer: Custom regex heuristics trained on Tamil Nadu Form 10 (e-Patta/Chitta).
• Entity Normalization: Automatically captures base survey numbers & sub-divisions (e.g. 102/1A, 104/2B).
• Area Unit Standardizer: Converts Hectares-Ares & Cents into Acres & Square Meters:
• Formula: Acres = (Hectares x 2.47105) + (Ares x 0.0247105)
• Classification: Categorizes Ryotwari Dry (Punjai), Wet (Nanjai), Natham, and restricted Poramboke.
ENGINE 2
FMB Ladder Vectorization Engine
File: backend/fmb_parser.py
• G-Line Baseline: Orients baseline of length L along azimuth angle theta from origin (x0, y0).
• Coordinate Triangulation for offset i at distance d_i with offset o_i:
• xi = x0 + d_i cos(theta) - o_i sin(theta)
• yi = y0 + d_i sin(theta) + o_i cos(theta)
• Shoelace Polygon Closure: Computes ground-truth FMB area: A = 0.5 x |Sum(x_i y_{i+1} - x_{i+1} y_i)|
ENGINE 3
Spatial Cadastral Reconciler
File: backend/spatial_engine.py
• MultiPolygon Centroids: Recursive flattening of nested rings to prevent coordinate NaN drift.
• 3-Way Variance Checking: Delta A% = |Area_Doc - Area_GIS| / Area_GIS x 100
• Permissible Margin: <= 2.0% Clean | 2%-5% Moderate | >5% Critical Flag
• Statutory Buffer Clipping: Shapely spatial intersection for 30m Waterbody and 15m Road RoW buffers.

## Slide 6
DEEP-DIVE ENGINES 4-6
Core Engines: Terrain Inundation, Risk Scoring & Ingestion
FarmAI Platform • Autonomous Due Diligence & Cadastral Reconciliation
CONFIDENTIAL • TEAM 63
ENGINE 4
Raster DEM & Terrain Inundation
File: backend/terrain_engine.py
• Elevation Extraction: Samples Copernicus / SRTM 30m Digital Elevation Models at parcel centroid.
• Slope Gradient Calculation: Slope % = (Delta Elevation / Delta Horizontal Run) x 100
• Hydrological Modeling: Compares against regional flood baseline (10m MSL):
• • Elevation < 12m & Slope < 1%: High Inundation Risk (Monsoon waterlogging)
• • Elevation 12m-20m: Moderate Risk | >20m: Safe
ENGINE 5
Title Integrity Risk Scorer
File: backend/risk_analyzer.py
• Base Score: 100 points maximum.
• Deduction Formula: Score = 100 - P_area - P_water - P_road - P_fmb - P_terrain
• Statutory Tiers:
• Tier 1 (85-100): Low Risk / Clean Title for bank lending
• Tier 2 (60-84): Moderate Risk / Requires Sub-Registrar Audit
• Tier 3 (0-59): Critical Risk / Title Rejected
ENGINE 6
Large Dataset Streaming Pipeline
File: backend/batch_ingestion.py
• 500MB+ Ingestion: Overcomes browser memory bottlenecks through chunked 8MB disk streaming.
• Concurrent Scanning: Recursively parses unstructured folder structures containing PDFs, TIFFs, and GeoJSONs.
• Deduplication Engine: SHA-256 file hashing ensures zero duplicate audit records.
• Progressive Loading: Streams parcels dynamically into Leaflet map without UI freeze.

## Slide 7
RISK QUANTIFICATION
Mathematical Risk Penalty Matrix (0–100)
FarmAI Platform • Autonomous Due Diligence & Cadastral Reconciliation
CONFIDENTIAL • TEAM 63
Parameter | Trigger Condition | Deduction | Statutory Rationale
Area Variance (P_area) | Delta A% > 5.0% discrepancy | -25 Points | Severe discrepancy between document claim and GIS boundary.
Area Variance (P_area) | 2.0% < Delta A% <= 5.0% | -10 Points | Moderate variance requiring physical re-survey audit.
Waterbody Buffer (P_water) | Encroaches within 30m buffer | -35 Points | Mandatory non-development zone under Supreme Court & NGT orders.
Road RoW Corridor (P_road) | Encroaches within 15m RoW | -15 Points | Highway expansion corridor violation / setback infringement.
FMB Boundary Skew (P_fmb) | FMB vs. Cadastral shape mismatch | -15 Points | Physical boundary ladder does not close onto cadastral map.
Flood Vulnerability (P_terrain) | Elevation < 12m MSL & slope < 1% | -10 Points | Hydrological depression prone to severe monsoon inundation.
TIER 1 (85–100)
LOW RISK / CLEAN TITLE
Passed all statutory checks. Recommended for bank lending, solar farm lease, or purchase.
TIER 2 (60–84)
MODERATE RISK / CAUTION
Minor boundary variance or setback warning. Requires physical surveyor verification.
TIER 3 (0–59)
CRITICAL RISK / REJECTED
Illegal waterbody encroachment or severe area inflation. Immediate red flag.

## Slide 8
EVALUATION & BENCHMARKS
Automated Pipeline Verification: 5 Benchmark Scenarios
FarmAI Platform • Autonomous Due Diligence & Cadastral Reconciliation
CONFIDENTIAL • TEAM 63
Doc ID | Survey No. | Benchmark Scenario | Calculated Variance / Violation | Audit Verdict
DOC-SAMPLE-01 | 102/1A | Clean Title Benchmark | Delta A% = 0.8% (Permissible), 0 Encroachments | LOW RISK (Clean Title)
DOC-SAMPLE-02 | 104/2B | Severe Area Mismatch | Claimed 4.5 Ac vs. GIS 3.1 Ac (Delta A% = +45%) | CRITICAL DISCREPANCY
DOC-SAMPLE-03 | 108/3 | Waterbody Encroachment | Intersects 30m protected Kanmoi lake buffer | CRITICAL / BUFFER BREACH
DOC-SAMPLE-04 | 110/1A | Road RoW Encroachment | Boundary intrudes 4.2m inside 15m road corridor | MAJOR DISCREPANCY
DOC-SAMPLE-05 | 112/1 | FMB Boundary Skew | FMB Ladder triangulation misaligned with Cadastral | MODERATE / AUDIT REQ.
100% Automated Pipeline Test Pass (backend/test_pipeline.py)
All 5 real-world stress test scenarios are validated automatically on every code push via GitHub Actions CI. The suite executes OCR text parsing, FMB vector coordinate computation, Shapely buffer intersection queries, and risk score thresholds in under 2.5 seconds.

## Slide 9
USER EXPERIENCE
Interactive Enterprise GIS & Frontend Experience
FarmAI Platform • Autonomous Due Diligence & Cadastral Reconciliation
CONFIDENTIAL • TEAM 63
Interactive Cadastral GIS Map
• High-resolution Esri World Imagery satellite basemap.
• Renders 396 parcel boundary polygons dynamically.
• Instant Centroid Fly-To when clicking any parcel in table.
• Multi-layer toggle: Waterbody 30m buffers, Roads, Infrastructure.
Multimodal Document Inspector
• Side-by-side view of scanned land deeds alongside extracted OCR entities.
• Field-by-field diff comparison between claimed vs. ground-truth data.
• Highlights discrepancies in red/amber badges directly on the document.
Due Diligence Certificate
• One-click generation of formal Land Audit Certificates.
• Includes surveyor signature block, GIS boundary thumbnail, risk breakdown, and tamper-evident SHA-256 audit hash.
• Exportable to PDF and print-ready formats.

## Slide 10
CLOUD & DEVOPS
AWS Cloud Architecture & Automated CI/CD Pipeline
FarmAI Platform • Autonomous Due Diligence & Cadastral Reconciliation
CONFIDENTIAL • TEAM 63
AWS Cloud Architecture (ap-south-1)
• Amazon Textract: DetectDocumentText API provides high-accuracy OCR for Tamil & English land deeds and tables. • Amazon S3 (fai-tce-team63-farmai): Encrypted cloud bucket storing ingested land deed PDFs, FMB sketches, and buffering multi-page documents. • Amazon DynamoDB: High-throughput NoSQL table (fai-tce-team63-audit-records) logging immutable audit scores, survey numbers, and verdicts. • Docker Deployment: Multi-container setup with backend FastAPI (port 8000) and Nginx frontend (port 80).
Automated GitHub Actions CI/CD
• Continuous Integration Workflow: Triggered on every push to main via .github/workflows/ci.yml. • Parallel Execution Runners: 1. Backend Job (Ubuntu + Python 3.11): Dependency caching, pip install, and automated test_pipeline.py execution. 2. Frontend Job (Ubuntu + Node.js 20): npm ci and production Vite build verification. • Zero Credential Exposure: AWS secrets securely injected via GitHub Encrypted Secrets with automatic log masking (***). • Build Health: Verified 100% green build status.

## Slide 11
BUSINESS VALUE & VISION
Business Impact & Technological Roadmap
FarmAI Platform • Autonomous Due Diligence & Cadastral Reconciliation
CONFIDENTIAL • TEAM 63
Measurable Business Impact
• 99% Faster Due Diligence
Reduces parcel cross-checking from 3-5 days to under 2 seconds per document.
• Zero Manual Math Errors
Automates complex G-line ladder triangulation and Hectares-to-Acres unit conversions.
• NPL & Legal Risk Prevention
Catches 30m waterbody buffer violations and area inflation before capital commitment.
• Institutional Audit Readiness
Generates tamper-evident digital certificates ready for banks, REITS, and government registrars.
Technological Roadmap
• Phase 1: Satellite Change Detection
Integrate Sentinel-2 & Planet Labs optical imagery to detect temporal tree canopy & encroachment changes.
• Phase 2: Fine-Tuned Tamil Vision Model
Train a domain-specific Donut / LayoutLMv3 vision transformer on historical Tamil revenue manuscripts.
• Phase 3: Drone LiDAR Elevation Mesh
Incorporate centimeter-precision UAV photogrammetry for flood runoff and terrain slope modeling.
• Phase 4: Blockchain Title Hashing
Anchor audit certificates onto Polygon / Hyperledger to prevent retroactive deed tampering.

## Slide 12
FarmAI – GeoLand Intelligence
Autonomous Multimodal GeoAI & Land Document Due Diligence Platform
Key Takeaways: - Solved the multimodal challenge: Unstructured Tamil/English deeds + FMB ladders + Cadastral GIS. - 100% automated mathematical due diligence with 6 specialized GeoAI engines. - Enterprise-grade cloud architecture with AWS Textract, S3, DynamoDB & GitHub Actions CI. - Production-ready interactive GIS dashboard built with React 18 and Leaflet.
Thank You! Questions & Discussion
GitHub Repository: https://github.com/krishnakanthm2805/farmai_project.git